## Slide 1: Physical Intent and abstractions
Nigel Davis (Ciena)
20230613

## Slide 2: Drivers…
Requirement: To set cost, risk and other impairment parameters on a link
  Cost, risk and other impairment parameters can only be determined by physical, geographical, power and network analysis and this cannot be performed by the devices of the network itself
  Cost and risk are determined in a planning and GIS environment (outside and above the controller)
  Some impairments need to be measured in the network to form a baseline, but the measurements may not be used directly and may be manipulated by planning tools
  A controller that is performing connectivity-service computation (and/or path computation) needs to understand cost and risk (along with other impairment parameters)
Observation:
  Risk is really present in the physical network and hence should be provided with physical intention
  Physical intention would provide other benefits from a planning perspective
  It is not always possible to provide physical intention
  Existing systems operate in a variety of ways in this area and these different ways of operating need to be accommodated

## Slide 3: Coverage
Entities considered
  Equipment
  PhysicalSpan
  Device
  Link
  Node
Non-discoverable properties such as cost and shared risk are provisioned with intention
  But this provisioning may be delegated to a lower controller

## Slide 4: Dependencies
In a real network and a realizable plan
  A Link can exist without a stated physical span, but it implies the presence of one or more real/realizable physical spans
  A node can exist without a stated device, but it implies the presence of one or more real/realizable devices
In a speculative plan any entity can exist alone, and the dependencies can be unresolved
The risk situation of a link/node depends upon the risk situation in the supporting physical network
  Abstract summary risk statements could be recorded on a link that only have a loose relationship to the real physical environment
  The link/node needs to override the risk statements from the physical environment
The cost statement is similar to risk but with a higher likelihood of loose abstraction
Other parameters may have a complex relationship to the actual physical environment requiring significant analysis and abstraction
The risk/cost/etc. statements on a physical span are derived from those of the strands but can be a loose abstraction
The model needs to allow for detailed cost/risk/etc. propagation but also to override the cost/risk propagation with a loose abstraction
There is a need for directional support for cost/risk/etc. in a bi-directional point-point and for detailed cost/risk/etc. statements in a multi-point (similar to node rules but applied to the link)

## Slide 5: Rough proposal
Consider physical intention
Consider link cost/risk override
Consider node risk/cost override using existing group rule structure

## Slide 6: Sketch of Physical Intention
Create/Delete/Edit intention
  Device
  Equipment
  PhysicalSpan
Intention will require a temporal dimension as well as a probabilistic dimension for speculative futures
  This can be handled by providing all Intention as lists and by adding properties that relate to time and speculation
  The temporal and speculative properties could be left for future development if the defaults are assumed to be FOR_ALL_FUTURE_FROM_NOW (temporal) and CERTAIN (probability)
  The basic feature will only require/allow a single element in the list
Intention states
  DETECTION: ACTUAL/FABRICATED/CONFIRMED/NOT_DETECTED/DETECTION_NOT_SUPPORTED
  PLAN: INTENDED/NOT_INTENDED/NO_INTENTION/INTENTION_NOT_SUPPORTED
  DELEGATED_PLAN: EXPECTED/NOT_EXPECTED/NO_EXPECTATION/EXPECTATION_NOT_SUPPORTED
  ADOPTION: isAutoExpectOnDetection, isAutoIntendOnDetection
  MISMATCH: ACTUAL_EXPECTED/ACTUAL_INTENDED/INTENDED_EXPECTED/ACTUAL_INTENDED_EXPECTED
  Cannot delete ACTUAL/FABRICATED/CONFIRMED
  Can adopt FABRICATED, ACTUAL and CONFIRMED to form INTENDED and/or EXPECTED
Approach for Device
  Add intention states to Device
  Duplicate subordinate property set with intended-actual mismatch structure
  UUID is created by provider
Approach for PhysicalSpan
  PhysicalSpan can have CONFIRMATION via discovery of client layer and perhaps with OTDR
  PhysicalSpan information can be fabricated
  Duplicate subordinate property set with mismatch
  Physical Span details (including abstract strands) cannot be discovered really, although OTDR could provide a potential confirmation-mismatch wrt splice statements (although abstract strand is not real span so OTDR would probably just be a parallel statement in the abstract strand space)
  UUID is created by provider
Approach for Equipment
  Add intention states to Equipment (where not already present)
  Intention should match expectation which is (delegated intention)
  Add mismatched
  Add intention structure that is the same as expectation structure
  UUID is created by provider

## Slide 7: Link propagation, intention, discovery and override
Link propagation
  Where an underlying network structure (physical or logical) gives rise to a link
    Server top level connection
    Physical Span
Link discovery
  Where an adjacency is determined through a protocol exchange between two CEPs which is propagated to
    The next level link above if the CEPs bound a top-level connection
    A link below the adjacency where it is “known” that there are no devices in the layer of the adjacency (therefore a link connection that is not serial-compound) between the two communicating CEPs
  Link discovery at the lowest layer next to physical (with NEPs that have associated access ports) may cause a fabricated physical span
Link intention
  Where physical network is unknown, but a higher layer system can provide a link abstraction of that network
  Link intention:
    Is created by the client system at the lowest layer of visibility
    May be created but then, as a result of network changes, conflict with link propagation/discovery
    At the lowest layer next to physical (with NEPs that have associated access ports) may cause a fabricated physical span
Link property override
  Where property values of the link that have been propagated from a lower layer (or are not present in a lower layer) are replaced by intended property values

## Slide 8: TAPI 2.5
Focus on PhysicalSpan and a lightweight Device
  Use Cases: Create/Edit/Delete PhysicalSpan
    Create Intention with cost/risk/etc. as INTENDED
    Delete when no NOT_DETECTED or DETECTION_NOT_SUPPORTED
    Edit state FABRICATED or CONFIRMED to add INTENDED
      Could create
      Could adopt (this would be a creation with an adoption property set)
      Note that FABRICATED is similar to expected, but suspect this is not sticky.
    Edit state to remove INTENDED from FABRICATED or CONFIRMED
      Could delete and this would result in the same thing perhaps
    Edit cost/risk/etc. on INTENDED
      Not FABRICATED: Simply edits parameters
      FABRICATED: Can set adoption parameter in edit to force FABRICATED to match INTENTION
    Edit cost/risk/etc. in FABRICATED
      Simply edits parameters
  Tolerate UUID change on PhysicalSpan
  Modify Device
    Edit cost/risk/etc. (this is essentially additional plan data)
Focus on Link
  Support link property override via edit of Link to apply override fabricated cost/risk/etc. parameters (substituting form the upward propagation of cost/risk/etc.)
  Use Cases: Create/Edit/Delete Link
    where the link is at the “lowest level” of visibility (especially the link next to physical)
  DETECTION: ACTUAL/FABRICATED/CONFIRMED/NOT_DETECTED/DETECTION_NOT_SUPPORTED
  PLAN: INTENDED/NOT_INTENDED/NO_INTENTION/INTENTION_NOT_SUPPORTED
  DELEGATED_PLAN: EXPECTED/NOT_EXPECTED/NO_EXPECTATION/EXPECTATION_NOT_SUPPORTED
  ADOPTION: isAutoExpectOnDetection, isAutoIntendOnDetection, isAutoExpectAndIntendOnDetection
  MISMATCH: ACTUAL_EXPECTED/ACTUAL_INTENDED/INTENDED_EXPECTED/ACTUAL_INTENDED_EXPECTED

## Slide 9: States in more detail
  DETECTION:
    ACTUAL: Detail read from the actual network (e.g., serial number of an equipment)
    FABRICATED: Detail constructed at the device or in a lower controller that is essentially delegated plan info (but not necessarily sticky
    CONFIRMED: Has just the defining parameters (e.g., just presence for an equipment or the two ends for a physical span)
    NOT_DETECTED: Detection available but nothing has been detected
    DETECTION_NOT_SUPPORTED: No opportunity for detection of actual or fabricated
  PLAN:
    INTENDED: Details from the plan
    NOT_INTENDED: Specifically intended to not be there
    NO_INTENTION: No statement as to whether the items should be there or not
    INTENTION_NOT_SUPPORTED: No opportunity for setting intention
  DELEGATED_PLAN: EXPECTED/NOT_EXPECTED/NO_EXPECTATION/EXPECTATION_NOT_SUPPORTED
    EXPECTED: Details from the plan owned by the subordinate controller (e.g., in the device)
    NOT_EXPECTED: Specifically expected to not be there
    NO_EXPECTATION: No statement as to whether the items should be there or not
    EXPECTATION_NOT_SUPPORTED: No opportunity for setting expectation
  ADOPTION: isAutoExpectOnDetection, isAutoIntendOnDetection, isAutoExpectAndIntendOnDetection
  MISMATCH: ACTUAL_EXPECTED/ACTUAL_INTENDED/INTENDED_EXPECTED/ACTUAL_INTENDED_EXPECTED

## Slide 10: Related topics
Setting/Editing/Removing impairment statements
  In CEP
  In profile
  In spec

## Slide 11: TAPI 2.5 proposal
Simple SET of properties on a link
  Properties are
    state: administrative-state: LOCKED/UNLOCKED , lifecycle-state: cannot be adjusted
    transfer-cost: list cost-name/cost-value/cost-algorithm set as required
    transfer-integrity: error-characteristic, loss-characteristic, repeat-delivery-characteristic, deliver-order-characteristic, unavailable-time-characteristic, sever-integrity-process-characteristic set as required
    transfer-timing: list latency-characteristics (expand this) set as required
    risk-parameter: list of risk-characteristics where risk-characteristic-name and risk-identifier-list are set as required
  Behaviour
    When a discovered link goes away configured data may be lost as there is no intent. If it is lost the client must reset when the link returns.
Creation of link “intent” where no discovery is available
  Properties are
    layer-protocol-name: PHOTONIC_MEDIA (NEP with supported CEP qualifier OTS_MEDIA)
    direction: set to BIDIRECTIONAL or UNIDIRECTIONAL (where directionality is determined by NEPs)
    resilience-type: restoration-policy: NA, protection-type: NO_PROTECTION
    node-edge-point: (list of 2 only)
    state: administrative-state: LOCKED/UNLOCKED , lifecycle-state: INSTALLED (note that the definitions of lifecycle-state are not adequate, should be INTENDED perhaps)
    {transfer-capacity: total-potential-capacity: , available-capacity: (RO, defined by NEPs)}
    transfer-cost: list cost-name/cost-value/cost-algorithm set as required
    transfer-integrity: error-characteristic, loss-characteristic, repeat-delivery-characteristic, deliver-order-characteristic, unavailable-time-characteristic, sever-integrity-process-characteristic set as required
    transfer-timing: list latency-characteristics (expand this) set as required
    risk-parameter: list of risk-characteristics where risk-characteristic-name and risk-identifier-list are set as required
    {validation: assumed not used as the physical link cannot be validated other than through a manual mechanism}
  Behaviour
    Discovery of a link that clashes with the intent will cause the provide to delete the intent
Link “intent” can be deleted
Link creation may give rise to an associated physical span
  Physical span content cannot be set in this release
  When the link is deleted so will the physical span be