## Slide 1: Path Constraints
Jonathan Sadler
Dec 8, 2023

## Slide 2: Path Constraints
Path Constraints are different than link constraints as they assess the whole candidate path and not just a single link
  Link Constraint example: Capacity
17
1
4
Capacity required = 3

## Slide 3: Path Constraints
Path Constraints are different than link constraints as they assess the whole path and not just a single link
  Link Constraint example: Capacity
  Path Constraint example: Latency
    Will adding this link cause me to exceed my latency limit?
17
1
4
LatencyINPUT = 10
LatencyMAX=25

## Slide 4: Why not just replace Cost with the Path Constraint?
The Goal is to compute the lowest cost link that complies with the path constraint
Dijkstra’s Cost is used to optimize (i.e. shortest path) the path being computed
  This means if the Cost is replaced with the attribute being used for the Path Constraint, the result will be optimized for that attribute.
    Replacing Cost with the Path Constraint attribute means a connection will use the path with the lowest aggregated attribute, independent of cost.
  Removing the “Cost” attribute means that the administrator does not have any “knobs” to bias traffic towards/away from specific links
Consider the following scenario:
17
1
4
LatencyINPUT = 10
LatencyMAX=25
5
9
10
A
C
B

## Slide 5: How can Path Constraints be used?
Initial example was Latency
  Important for some services that are Latency sensitive
    Example: Fiber Channel has buffer size limitations which become problems when latency is high.
  Also Important for some services that want data delivered as fast as possible
    Example: Chicago-New York fiber route used for arbitrage trading
Other Examples
  Optical Impairments limiting OSNR
    Per candidate computed impairments can determine if a candidate is compliant or not
      Computed impairment recognizes that many optical impairments are not simple linear calculations (e.g. RMS, dB summation)
  Chromatic Dispersion limiting optical receiver
Treating Path Constraints as constraints (instead of costs) makes it possible to handle multiple constraints at the same time
  Don’t have to deal with multiple simultaneous optimizations

## Slide 6: Dijksta modifications necessary?
Need to look into this.