## Slide 1: Review of TAPI 2.5.0
Andrea Mazzini, Nokia
February 26, 2024

## Slide 2
TapiPhotonicMedia: The application code is not included in 2.5.0 OtsiConfigPac
  Impact: regression from 2.1.3, not possible to specify this parameter Possible solutions:
  2.5.0: add explanation in RIA 3.2
    consider what available in 2.1.3 - allow to maintain the 2.1.3 augment (OtsiTerminationConfigPac), or
    add the missing parameter(s) to the OtsiConfigPac name-value pairs
  2.5.1/2.6.0: restructure the OtsiConfigPac together with the TransceiverProfile
The photonic CEP does not include center/edge frequency constraint (adjustment granularity, grid type)
  Impact: regression from 2.1.3, not possible to get this parameter
  Possible solutions:
  2.5.0: add explanation in RIA 3.2
    add the missing parameter(s) to the CEP name-value pairs
  2.5.1/2.6.0: add the missing parameter to proper augmentation
Bugs - Regressions

## Slide 3
TapiConnectivity: ConnectionAndRouteConstraint augments only
  ConnectivityService/TopologyConstraint, but not
  ConnectivityService/ResilienceConstraint/ResiliencyRouteConstraint/TopologyConstraint
  Impact: new feature not yet described in RIA, not possible to provision Connection/Route constraints specific for the single (resiliency) Route
  Possible solutions:
  2.5.0: add explanation in RIA 3.2
    add the missing parameter(s) to the TopologyConstraint name-value pairs
  2.5.1/2.6.0: add the missing augment
Bugs – Incomplete features 1/2

## Slide 4
TapiConnectivity: SwitchOperation, which augments Connectivity Service, the SwitchDirection (BID, SINK SOURCE) is not appropriate on Connectivity Service base.
  Impact: new feature not yet described in RIA, it is not possible to provision a manual operator command on only one direction of a bidirectional Connectivity Service Possible solution:
  The identification of one direction of a bidirectional Connectivity Service is possible only listing the CSEPs in the proper order. Introduce the A/Z paradigm?
Bugs – Incomplete features 2/2
1, 2
2, 1
ROADM
Amplifier
OLP1
OLP2
PHOTONIC
OTS_MEDIA
OMS Top Connection (degree to degree port)
ROADM
OTS_MEDIA Top Connection
OMS
OTS
OTS
ROADM
ROADM
MC Top Connection (degree to degree port)
MC Connectivity Service
MC Connectivity Service
OMS Connectivity Service
1
2
OTS_MEDIA
PHOTONIC
OMS
PHOTONIC
MC
PHOTONIC
OTSiMC
PHOTONIC

## Slide 5
OTSiMCA CS – Decoupling of L0 and L1 parameters, to allow more variations of L1 payload
Clarify min/max power on OtsiConfig (transceiver), always a range or single value?
Additional UNI scenario for multi-technology ports
Correction of incorrect statement in RIA 3.1:
  Table 38: Connection-end-point (CEP) object definition, in case of not terminated CEP, there is not a client NEP.
More Urgent Improvements – only on RIA (3.2)
client-node-edge-point | List of { node-edge-point-ref } | RO | M | Provided by tapi-server This RIA only considers CEP instances supporting a single client NEP.

## Slide 6
Centralized and distributed capabilities, centralized and distributed provisioning
  Always allow both solutions in the YANG, and recommend Profiles in the RIA?
  In case of centralized, how to possibly edit the properties of the entity referring the profile?
  Invariant profiles are preferred
Add the DIGITAL_SIGNAL_TYPE_FC_1000 (https://fibrechannel.org/roadmap/)
In the Access Port the device uuid in the pin seems redundant, as the device instance is always the same of the Access Port.
Other improvements 1/2
+--rw physical-context
+--ro device* [uuid]
| +--ro equipment* [uuid]
...
| +--ro access-port* [uuid]
| | +--ro connector-pin* [device-uuid equipment-uuid connector-identification pin-identification]
| | | +--ro connector-identification string
| | | +--ro pin-identification string
| | | +--ro pin-and-role* [location-in-connector]
| | | | +--ro location-in-connector string
| | | | +--ro pin-role* string
| | | | +--ro pin-name? string
| | | | +--ro connector-pin-orientation? connector-and-pin-orientation
| | | +--ro device-uuid -> /tapi-common:context/tapi-equipment:physical-context/device/uuid
| | | +--ro equipment-uuid -> /tapi-common:context/tapi-equipment:physical-context/device/equipment/uuid
| | +--ro profile* [profile-uuid]
| | | +--ro profile-uuid -> /tapi-common:context/profile/uuid
| | +--ro uuid uuid
| | +--ro name* [value-name]
| | +--ro value-name string
| | +--ro value? string
| +--ro uuid uuid
| +--ro name* [value-name]
| +--ro value-name string
| +--ro value? string
grouping access-port {
list connector-pin {
key 'device-uuid equipment-uuid connector-identification pin-identification';
/* the reference to equipment is used as a key, but the key statement does not accept container, but only leafs.
Hence the two leafs of the equipment-ref have been explicitly specified.*/
config false;
min-elements 1;
uses connector-pin-address;
description "The list of Pins that support the AccessPort.";
}

## Slide 7
Other improvements 2/2
Bidirectional Links ended by 4 unidirectional NEPs / Bidirectional Connections ended by 4 unidirectional CEPs
Versioning the context of YANG module, i.e. additional info besides "revision", which is a date.
  In https://datatracker.ietf.org/doc/html/draft-ietf-netmod-yang-module-versioning-10 it is advised to
  add a “revision label” using a hasth tag, e.g. tapi-common#2.5.0.yang
  add the option “rev:revision-label”
  support ietf-yang-library-revisions
  Hence until module versioning becomes an RFC, there is no simple way to tag with semàntic versioning a module and naming the module set seems to be a quasi manual operation.

## Slide 8
Other possible future enhancements 1/2
Allow to list more layerProtocolName values in the Notification parameters. E.g., for multi-layer Nodes.
Allow to list more layerProtocolQualifier values in the CEPs – multi-layer CEP
  Possibly solved by adding the proper augments (e.g. ODU CEP including the OTU augment)
To be considered an attribute like MCA ID for the MC CEPs.
(Not terminated) OTSiMCA and MCA monitoring point common for more NMCs / MCs
OTSiA monitoring point common for more OTSi (OTSiG-O MIP/NIM also in Photonic Domain)
  From 2.3, solved with OtsiaMep, pac of OtuMep (i.e. when OTSiMCA is encapsulated in OTU CEP)
  2.5.1/2.6.0, solved by OTSiMCA CS (i.e. when OTSiMCA CEP is decoupled from OTU/ODU CEP)

## Slide 9
Consider stereotype for conditional/mandatory statements – to be translated into Yang at least as a comment.
  “feature” and “if-feature” yang statements and “support/condition” stereotype params.
Set systematically as "Is read only" all resource attributes
There are two distinct ”PortRole” types, resp in TapiCommon and TapiTopology.
Issue regarding the translation of UML [n..*], only for n=1, to YANG "min-elements n".
Issue of connection-ref and path-ref, which cannot be used because the connection and path yang nodes are read-only hence cannot be referred by a read-write list (of a provisioning data structure).
  The "require-instance" (https://datatracker.ietf.org/doc/html/rfc7950#section-9.9.3) set to false may solve the issue.
Some enum issues:
  CapacityPac
    Capacity-unit enum should be identity
    Capacity-value should be string
  Mapping type in the ODU should be identity
Allow Link to have only one end NEP, for UNI/ENNI cases.
Other possible future enhancements 2/2

## Slide 10
BACKUP

## Slide 11
Enhance Equipment Model: Closed, see minutes 2020-03-24 TAPI Meeting notes
  three different scenarios are considered:
  "Division": The equipment slot (and sub-slot) structure is fixed: there is only one level of Holder objects, which may represent both "full slot" space or "sub slot" space cases. In other words, the Holder always represents the smallest granularity occupance model (as per current definition).
  "Hierarchy": The equipment slot structure can evolve: an additional level of "SubHolder" objects is introduced. The SubHolder class inherits from Holder and is introduced only to avoid Holder recursion, which is difficult to manage in YANG. This SubHolder object is used when an existing Holder object instance, representing a full slot space, needs to be decomposed into more "sub slot" spaces.
  "Specific Hw": Same as case 2. above, but (management information about) specific hardware is necessary to implement "sub-slotting". In this case, the existing Holder object will host an Equipment object (either reusing category SUBRACK or adding a new enum, e.g. SUBSLOT) which in turn "HasHolders" (the sub-slots).
Equipment - solved

## Slide 12
Version used: https://github.com/karthik-sethuraman/EagleUmlYang/tree/Tapi_v2x
ExtendedComposite stereotype:
  Applicable only to 1:1 associations
  In YANG the attributes of the composed class become attributes of the composing class
  The composed class does not appear in YANG
StrictComposite stereotype:
  Applicable to any association (1:* etc.)
  In YANG translates the composition into “uses” statement
  Necessary for the version of the tool used
    ITU-T Q14/15 uses a different version
Tested a more advanced version of the tool – but not enough pros wrt to the cost of migration
Note on UML to YANG Tool