## Slide 1: TAPI Lifecycle State Of Connectivity Services
Andrea Mazzini, Nokia
September 13, 2023

## Slide 2
Definitions
6.2.3.3 Staged Provisioning (Experimental)
The connectivity service creation could be performed in a staged way, to enable a more controlled reservation and configuration of network resources. It is not foreseen a staged removal of a connectivity service.
The reservation of resources should be temporary in the process of service provisioning, in other words mechanisms utilizing temporal expressions may release the resources in a timely manner.

## Slide 3
Definitions
Creation of the connectivity service:
  The object is created through proper POST API, with lifecycle state “PLANNED”.
  The “PLANNED” lifecycle state indicates that the server controller has at least checked the general feasibility of the request, including the reservation of end port bandwidth (SIP and NEP).
  No configuration of network resources.
  The following attributes of SIP and NEP have been updated:
    available-capacity
    ??
  It is intended that the reservation of end port bw should be propagated to any other controller competing for the same resources, e.g., a control plane.
  In case of failure, the connectivity service is not created, and an error response is provided.
  Admission control wrt Node throughput control resource availability to support the connection/switching request.
Network configuration of the connectivity service:
  The lifecycle state is moved from “POTENTIAL_AVAILABLE” to “POTENTIAL_BUSY”, through proper PUT API.
  The “POTENTIAL_BUSY” lifecycle state indicates that the server controller has successfully configured all the network resources.
  The following information are available:
    List of nodes in the route / more details??
    ??
  In case of failure, the connectivity service remains in “POTENTIAL_AVAILABLE” state and an error response is provided. Actions beyond this point depend upon controller implementation choices and operator policy.
Routing of the connectivity service:
  The lifecycle state is moved from “PLANNED” to “POTENTIAL_AVAILABLE”, through proper PUT API.
  The “POTENTIAL_AVAILABLE” lifecycle state indicates that the server controller has found and reserved a route in the network for the connectivity service.
  No configuration of network resources.
  The following information are available:
    List of nodes in the route??
    ??
  It is intended that the reservation of the route should be propagated to any other controller competing for the same resources, e.g., a control plane.
  In case of failure, the connectivity service remains in “PLANNED” state and an error response is provided. It is allowed to retry the operation or delete the connectivity service.
Commissioning of the connectivity service:
  The lifecycle state is moved from “POTENTIAL_BUSY” to “INSTALLED”, through proper PUT API.
  The “INSTALLED” lifecycle state indicates that the server controller has enabled the usage of the connectivity service.
  This enabling may or may not have involved configuration of network resources.
  All the information are available (Connections, Route, etc.).
  In case of provisioning failure, the connectivity service remains in “POTENTIAL_BUSY” state and an error response is provided. Actions beyond this point depend upon controller implementation choices and operator policy.
  In general, no check is performed by the provisioning process regarding network state (alarms, TCAs, etc.) The possible network failures are managed by Fault Management / Assurance applications.

## Slide 4
N
Y
Y
Set to P_A
Y
Set to P_B
Set to Inst
Y
Lifecycle State Diagram
PLANNED
Failed
Start
Success
Success
Create
Delete
Delete
Set to P-A
N
POTENTIAL_AVAILABLE
Failed
Success
Delete*
Delete
Not Specified
N
POTENTIAL_BUSY
Failed
Success
Delete*
Delete*
Not Specified
N
INSTALLED
end
Delete
A possible “direct creation in installed state” may be accepted but anyway the CS could transit through all the defined states.
PARTIAL
PARTIALLY_INSTALLED
Delete*