## Slide 1: Brief analysis of TAPI-IETF model linkage
Nigel Davis
20230124 (enhanced 20230131)
{This document contains notes and sketches and is not complete}

## Slide 2: Content
Solution architecture options
  These slides were added during the call as a result of a request for the context of the discussion
RFC8345 Model sketch
Diagram key and rough notes
Pictorial view of IETF/TAPI controlled network fragment
Focus on the key association with yang sketch
Further notes working towards additional associations
Purpose: To show an approach to linking between IETF models and TAPI where both are being used to manage the same single network

## Slide 3: Solution Architecture Option A
Orchestrator
IP
IP&P
P
P
IP
(2)
(1)
IETF
IETF
TAPI
(3)
TAPI
Covered by the proposal in this .pptx

## Slide 4: Solution Architecture Option B
Orchestrator
IP
IP&P
P
P
IP
P (3)
(1)
IETF
IETF
TAPI
(4)
TAPI
IP (2)
Partly covered by the proposal in this .pptx

## Slide 5: Solution Architecture Option C
Orchestrator
IP
IP
P
P
IP
P (3)
(1)
IETF
IETF
TAPI
(4)
TAPI
IP (2)
Partly covered by the proposal in this .pptx
P

## Slide 6: Solution Architecture Option D
Orchestrator
IP
IP
P
P
IP
P (3)
(1)
IETF
IETF
TAPI
(4)
TAPI
IP (2)
IETF
IP&P
(plug)
Covered by the proposal in this .pptx

## Slide 7: Solution Architecture Option E
Orchestrator
IP
IP&P
P
P
IP
P(3)
IP (1)
IETF
IETF
TAPI
(4)
TAPI
IP&P (2)
Covered by the proposal in this .pptx

## Slide 8: Solution Architecture Option F
Orchestrator
IP
IP&P
P
P
IP
P
IETF
TAPI
TAPI
IP&P
Covered by the proposal in this .pptx

## Slide 9: Solution Architecture Option G
Controller
IP
IP&P
P
P
IP
OC
Service
Multi - J

## Slide 10: RFC8345 Model sketch
network
node
supporting-node
termination-point
link
source-tp
destination-tp
supporting-termination-point
supporting-link
"A network link connects a local (source) node and
a remote (destination) node via a set of the respective
node's termination points. It is possible to have several
links between the same source and destination nodes.
Likewise, a link could potentially be re-homed between
termination points. Therefore, in order to ensure that we
would always know to distinguish between links, every link
is identified by a dedicated link identifier. Note that a
link models a point-to-point link, not a multipoint link.";
"This list identifies any termination points on which a
given termination point depends or onto which it maps.
Those termination points will themselves be contained
in a supporting node….. “
Not clear if termination points are unidirectional
(like link) or may be bidirectional.

## Slide 11: Diagram Key and rough notes
RFC8345 TP
RFC8345 Link
RFC8343 Interface
RFC8343 Interface with CEP like properties
RFC8299 site =~ access-port / SIP / CSEP
RFC9182
VPN Node
RFC9182 vpn-service =~ top connection
VRF (RFC4364/RFC8529)
RFC9182 vpn-network-access interface-id and tp
container vpn-network-accesses {
description
"List of network accesses.";
list vpn-network-access {
key "id";
description
"List of network accesses.";
leaf id {
type vpn-common:vpn-id;
description
"Identifier for the network access.";
}
leaf interface-id {
vpn-service
vpn-node
vpn-network-access
interface-id
connection
termination-point
Connection: Represents and groups the set of Layer 2 connectivity from where the traffic of the L3VPN in a particular VPN network access is coming.
RFC8299 (VRF allocation)… As for route targets (RTs), a management system is expected to allocate a VRF on the target PE and an RD for this VRF.
vpn-node':
  An abstraction that represents a set of policies applied to a network node and belonging to a single 'vpn-service'. A VPN service is typically built by adding instances of 'vpn-node' to the 'vpn-nodes' container.¶
  A 'vpn-node' contains 'vpn-network-accesses', which are the interfaces attached to the VPN by which the customer traffic is received. Therefore, the customer sites are connected to the 'vpn-network-accesses'.¶
For example, in a BGP-based VPN, a VPN node could typically be mapped to a Virtual Routing and Forwarding (VRF) instance.¶
Note that as there appears to be no clear standard way to represent networking defined in terms of IETF models, a symbol set for IETF models has been derived from the TAPI symbol set (familiarity with the TAPI symbol set as used in TR-547 is assumed)

## Slide 12: Pictorial view of IETF/TAPI controlled network fragment
Orientation Seems incorrect in RFC9182
Assumption on this figure is that layers up to Ethernet are managed through TAPI and IP is controlled through IETF defined interfaces. There are clearly many other options. This diagram simply illustrates a generalized linkage between RFC8345 and TAPI that could be applied at any layer.
Controlled through IETF interfaces
Controlled through TAPI

## Slide 13: Focus on the key association with yang sketch
TAPI CEP
RFC8345 TP
tapi-ietf-cep-extensions…
…
import ietf-network {
prefix nw;
reference
"RFC 8345: A YANG Data Model for Network Topologies";
}
…
list client-rfc8345-termination-point {
key “rfc8345-tp-id";
config false;
description “An RFC8345 termination point can terminate an RFC8345 link.”
leaf rfc8345-tp-id {
uses nw:tp-id;
description "This attribute provides the reference to the corresponding client TP
(equivalent to a TAPI NEP). Note that the TP is unidirectional, hence the list will contain
two references for a bidirectional CEP. ";
}
}
tapi-tp-extensions… {need to understand standard convention for naming extensions}
augment “...rfc8345 tp…" {
container supporting-tapi-cep {
uses tapi-connectivity:cep-list; connection-end-point-ref;
description "This augment allows RFC8345 TP to refer to a TAPI CEPs. This list identifies any
TAPI CEPs onto which it maps (directly depends).
This dependency information cannot be inferred from the dependencies between links
as no interlink reference is provided between models.";
}
description “…";
}
Bidirectional
RX
TX
Extension to RFC8345 as an augmentation maintained by ONF TAPI
Extension to TAPI as an augmentation maintained by ONF TAPI

## Slide 14: Alternative using shared value
TAPI CEP
RFC8345 TP
tapi-ietf-cep-extensions…
…
import ietf-network {
prefix nw;
reference
"RFC 8345: A YANG Data Model for Network Topologies";
}
…
list tapi-rfc8345-shared-resource-ref {
key “rfc8345-tp-id";
config false;
description “An RFC8345 termination point can terminate an RFC8345 link.”
leaf tapi-rfc8345-shared-resource-ref {
type string;
config false;
description “Will have a value that can also be found in the corresponding attribute of the TAPI CEP”;
}
description " description "This attribute provides the reference to the corresponding client TP
(equivalent to a TAPI NEP). Note that the TP is unidirectional, hence the list will contain
two references for a bidirectional CEP. ";
}
}
tapi-tp-extensions… {need to understand standard convention for naming extensions}
augment “...rfc8345 tp…" {
container supporting-tapi-cep {
leaf tapi-rfc8345-shared-resource-ref {
type string;
config false;
description “Will have a value that can also be found in the corresponding attribute of the TAPI CEP”;
}
description "This augment allows RFC8345 TP to refer to a TAPI CEPs. This list identifies any
TAPI CEPs onto which it maps (directly depends).
This dependency information cannot be inferred from the dependencies between links
as no interlink reference is provided between models.";
}
description “…";
}
Bidirectional
RX
TX
Extension to RFC8345 as an augmentation maintained by ONF TAPI
Extension to TAPI as an augmentation maintained by ONF TAPI

## Slide 15: Further notes working towards additional associations
Termination Point: IETF Yang is ambiguous… From RFC8345:
"A termination point can terminate a link.
Depending on the type of topology, a termination point
could, for example, refer to a port or an interface.";
Interface: RFC8343 provides definition of an interface which suggests that it is a hybrid entity. The interface appears to have content that might be expected in a CEP (leaf speed (units "bits/second“), leaf in-octets (counter64)), but it also has properties that might be in an AccessPort as it has an appendix section with the following (ambiguous) statement:
  In this example, a router has support for 4 line cards, each with 8 ports. The slots for the cards are physically numbered from 0 to 3, and the ports on each card from 0 to 7. Each card has Fast Ethernet or Gigabit Ethernet ports.
  The device-specific names for these physical interfaces are "fastethernet-N/M" or "gigabitethernet-N/M". The name of a VLAN interface is restricted to the form "<physical-interface-name>.<subinterface-number>".
Physical: RFC8343 uses the word “physical” for non-physical things.
Termination Point: RFC8346 has a termination point property grouping l3-termination-point-attributes that provides some linkage to interface.
augment /nw:networks/nw:network/nw:node/nt:termination-point:
+--rw l3-termination-point-attributes
+--rw (termination-point-type)?
+--:(ip)
| +--rw ip-address* inet:ip-address
+--:(unnumbered)
| +--rw unnumbered-id? uint32
+--:(interface-name)
+--rw interface-name? string
RFC8299 has site which seems to blur with access-port, SIP and CSEP. The RFC states in an example (“Interaction with Other YANG Models”) that:
“In the service example above, the service component is expected to request that the configuration component of the management system provide the configuration of the service elements.” MCP will receive the service request and will translate that into a network realization. The network realization will be in terms of Interface
RFC8299 has service…