## Slide 1: Various TAPI associations
Nigel Davis
20240514

## Slide 2: Content
Node to device linkage
  Essential model and rules
Linkage between IETF and TAPI modesl
  RFC8345 Model sketch
  Diagram key and rough notes
  Pictorial view of IETF/TAPI controlled network fragment
  Focus on the key association with yang sketch
  Further notes working towards additional associations
Purpose: To show an approach to linking between IETF models and TAPI where both are being used to manage the same single network

## Slide 3: Node to device linkage
Currently, in TR-547, each node only relates to one device and is fully embraced by that device
  The mode allows for a node to spread across many devices, but this is not taken advantage of in TR-547
It is possible to navigate from a node via the related NEPs and associated Access Ports to the device
  But this navigation is overly complex for the simple cases
A list reference property from node to device and a corresponding property from device to node is proposed
  These properties are conditional
  These properties should be populated where the device relates to one or more nodes, but the node only relates to one device
    Where the node relates to only one device, the node is fully supported by that devic
  The properties are optional for other cases

## Slide 4: Linkage between IETF and TAPI models
This feature applies where a controller is exposing IP capabilities via an IETF model based on RFC8345 and photonics/OTN based on TAPI

## Slide 5: Diagram Key and rough notes
RFC8345 TP
RFC8345 Link
RFC8343 Interface
RFC8343 Interface with CEP like properties
RFC8299 site =~ access-port / SIP / CSEP
RFC9182
VPN Node
RFC9182 vpn-service =~ top connection
VRF (RFC4364/RFC8529)
RFC9182 vpn-network-access interface-id and tp
container vpn-network-accesses {
description
"List of network accesses.";
list vpn-network-access {
key "id";
description
"List of network accesses.";
leaf id {
type vpn-common:vpn-id;
description
"Identifier for the network access.";
}
leaf interface-id {
vpn-service
vpn-node
vpn-network-access
interface-id
connection
termination-point
Connection: Represents and groups the set of Layer 2 connectivity from where the traffic of the L3VPN in a particular VPN network access is coming.
RFC8299 (VRF allocation)… As for route targets (RTs), a management system is expected to allocate a VRF on the target PE and an RD for this VRF.
vpn-node':
  An abstraction that represents a set of policies applied to a network node and belonging to a single 'vpn-service'. A VPN service is typically built by adding instances of 'vpn-node' to the 'vpn-nodes' container.¶
  A 'vpn-node' contains 'vpn-network-accesses', which are the interfaces attached to the VPN by which the customer traffic is received. Therefore, the customer sites are connected to the 'vpn-network-accesses'.¶
For example, in a BGP-based VPN, a VPN node could typically be mapped to a Virtual Routing and Forwarding (VRF) instance.¶
Note that as there appears to be no clear standard way to represent networking defined in terms of IETF models, a symbol set for IETF models has been derived from the TAPI symbol set (familiarity with the TAPI symbol set as used in TR-547 is assumed)

## Slide 6: Pictorial view of IETF/TAPI controlled network fragment
Orientation Seems incorrect in RFC9182
Assumption on this figure is that layers up to Ethernet are managed through TAPI and IP is controlled through IETF defined interfaces. There are clearly many other options. This diagram simply illustrates a generalized linkage between RFC8345 and TAPI that could be applied at any layer.
Controlled through IETF interfaces
Controlled through TAPI

## Slide 7: Focus on the key association with yang sketch
TAPI CEP
RFC8345 TP
tapi-ietf-cep-extensions…
…
import ietf-network {
prefix nw;
reference
"RFC 8345: A YANG Data Model for Network Topologies";
}
…
list client-rfc8345-termination-point {
key “rfc8345-tp-id";
config false;
description “An RFC8345 termination point can terminate an RFC8345 link.”
leaf rfc8345-tp-id {
uses nw:tp-id;
description "This attribute provides the reference to the corresponding client TP
(equivalent to a TAPI NEP). Note that the TP is unidirectional, hence the list will contain
two references for a bidirectional CEP. ";
}
}
tapi-tp-extensions… {need to understand standard convention for naming extensions}
augment “...rfc8345 tp…" {
container supporting-tapi-cep {
uses tapi-connectivity:cep-list; connection-end-point-ref;
description "This augment allows RFC8345 TP to refer to a TAPI CEPs. This list identifies any
TAPI CEPs onto which it maps (directly depends).
This dependency information cannot be inferred from the dependencies between links
as no interlink reference is provided between models.";
}
description “…";
}
Bidirectional
RX
TX
Extension to RFC8345 as an augmentation maintained by ONF TAPI
Extension to TAPI as an augmentation maintained by ONF TAPI
Need to account for the uni-bi multi-point work on RFC8345 in IETF.
May need to be a list to account for the RFC8345 bi  TAPI uni case.

## Slide 8: Alternative using shared value
TAPI CEP
RFC8345 TP
tapi-ietf-cep-extensions…
…
import ietf-network {
prefix nw;
reference
"RFC 8345: A YANG Data Model for Network Topologies";
}
…
list tapi-rfc8345-shared-resource-ref {
key “rfc8345-tp-id";
config false;
description “An RFC8345 termination point can terminate an RFC8345 link.”
leaf tapi-rfc8345-shared-resource-ref {
type string;
config false;
description “Will have a value that can also be found in the corresponding attribute of the TAPI CEP”;
}
description " description "This attribute provides the reference to the corresponding client TP
(equivalent to a TAPI NEP). Note that the TP is unidirectional, hence the list will contain
two references for a bidirectional CEP. ";
}
}
tapi-tp-extensions… {need to understand standard convention for naming extensions}
augment “...rfc8345 tp…" {
container supporting-tapi-cep {
leaf tapi-rfc8345-shared-resource-ref {
type string;
config false;
description “Will have a value that can also be found in the corresponding attribute of the TAPI CEP”;
}
description "This augment allows RFC8345 TP to refer to a TAPI CEPs. This list identifies any
TAPI CEPs onto which it maps (directly depends).
This dependency information cannot be inferred from the dependencies between links
as no interlink reference is provided between models.";
}
description “…";
}
Bidirectional
RX
TX
Extension to RFC8345 as an augmentation maintained by ONF TAPI
Extension to TAPI as an augmentation maintained by ONF TAPI

## Slide 9: Further notes working towards additional associations
Termination Point: IETF Yang is ambiguous… From RFC8345:
"A termination point can terminate a link.
Depending on the type of topology, a termination point
could, for example, refer to a port or an interface.";
Interface: RFC8343 provides definition of an interface which suggests that it is a hybrid entity. The interface appears to have content that might be expected in a CEP (leaf speed (units "bits/second“), leaf in-octets (counter64)), but it also has properties that might be in an AccessPort as it has an appendix section with the following (ambiguous) statement:
  In this example, a router has support for 4 line cards, each with 8 ports. The slots for the cards are physically numbered from 0 to 3, and the ports on each card from 0 to 7. Each card has Fast Ethernet or Gigabit Ethernet ports.
  The device-specific names for these physical interfaces are "fastethernet-N/M" or "gigabitethernet-N/M". The name of a VLAN interface is restricted to the form "<physical-interface-name>.<subinterface-number>".
Physical: RFC8343 uses the word “physical” for non-physical things.
Termination Point: RFC8346 has a termination point property grouping l3-termination-point-attributes that provides some linkage to interface.
augment /nw:networks/nw:network/nw:node/nt:termination-point:
+--rw l3-termination-point-attributes
+--rw (termination-point-type)?
+--:(ip)
| +--rw ip-address* inet:ip-address
+--:(unnumbered)
| +--rw unnumbered-id? uint32
+--:(interface-name)
+--rw interface-name? string
RFC8299 has site which seems to blur with access-port, SIP and CSEP. The RFC states in an example (“Interaction with Other YANG Models”) that:
“In the service example above, the service component is expected to request that the configuration component of the management system provide the configuration of the service elements.” MCP will receive the service request and will translate that into a network realization. The network realization will be in terms of Interface
RFC8299 has service…